## Slide 1: Module #8: Transfer Path Analysis

## Slide 2: TPA: Outline
Introduction to TPA
Source-Path-Receiver Framework
Theory for TPA Methods
  Classical TPA
  Component-based TPA

## Slide 3: Introduction to TPA

## Slide 4: What’s the Point of TPA?
How is vibration energy moving in the system?
Troubleshooting undesired vibration responses:
  System sensitivities?
  High forces?
  Key contributors?
What happens if I change the system configuration?
We want a modular technique to understand noise and vibration in systems

## Slide 5: What’s the Point of TPA?
How is vibration energy moving in the system?
Troubleshooting undesired vibration responses:
  System sensitivities?
  High forces?
  Key contributors?
What happens if I change the system configuration?
We want a modular technique to understand noise and vibration in systems

## Slide 6: What’s the Point of TPA?
How is vibration energy moving in the system?
Troubleshooting undesired vibration responses:
  System sensitivities?
  High forces?
  Key contributors?
What happens if I change the system configuration?
We want a modular technique to understand noise and vibration in systems

## Slide 7: What’s the Point of TPA?
How is vibration energy moving in the system?
Troubleshooting undesired vibration responses:
  System sensitivities?
  High forces?
  Key contributors?
What happens if I change the system configuration?
We want a modular technique to understand noise and vibration in systems

## Slide 8: What’s the Basic Concept?
TPA takes a holistic perspective, by combining the responses, forces, and underlying physics for the noise and vibration
Noise and Vibration Responses
Modal Properties
Forces
The vibration data we care about

## Slide 9: Describing Noise and Vibration with Physics
We want to define all the elements in the equation of motion for our system

## Slide 10: Describing Noise and Vibration with Physics
Characterized by operating tests
We want to define all the elements in the equation of motion for our system

## Slide 11: Describing Noise and Vibration with Physics
Characterized by operating tests
Estimated with lab (e.g., modal) tests or numerical models
We want to define all the elements in the equation of motion for our system

## Slide 12: Describing Noise and Vibration with Physics
Characterized by operating tests
Estimated with lab (e.g., modal) tests or numerical models
Indirectly estimate the forces in most situations
We want to define all the elements in the equation of motion for our system

## Slide 13: Describing Noise and Vibration with Physics
Characterized by operating tests
Estimated with lab (e.g., modal) tests or numerical models
Indirectly estimate the forces in most situations
We want to define all the elements in the equation of motion for our system
Three different techniques

## Slide 14: Lingo Soup with TPA
Hybrid TPA
Component Based TPA
Classical TPA
Pseudo Forces
Blocked Forces
Contact Forces
Free-velocity Forces
Source
Paths
Receivers
Indicators
Contribution Analysis
Equivalent Source
Target
Virtual Prototype

## Slide 15: Different Types of TPA
Transfer Path Analysis
Classical TPA
Component Based TPA
Direct Force Measurement
Mount Stiffness Method
Matrix Inversion Method
Operational TPA
Free Velocity
Blocked Forces
In-situ Forces
Equivalent Source
Pseudo Forces
Matrix Inversion Method with Transmissibility Functions
Other Methods

## Slide 16: Different Types of TPA
Transfer Path Analysis
Classical TPA
Component Based TPA
Direct Force Measurement
Mount Stiffness Method
Matrix Inversion Method
Operational TPA
Free Velocity
Blocked Forces
In-situ Forces
Equivalent Source
Pseudo Forces
Matrix Inversion Method with Transmissibility Functions
Other Methods
Left out for brevity

## Slide 17: Different Types of TPA
Transfer Path Analysis
Classical TPA
Component Based TPA
Direct Force Measurement
Mount Stiffness Method
Matrix Inversion Method
Operational TPA
Free Velocity
Blocked Forces
In-situ Forces
Equivalent Source
Pseudo Forces
Matrix Inversion Method with Transmissibility Functions
Other Methods
Left out for brevity
Troubleshooting
Evaluating configuration changes

## Slide 18: Source-Path-Receiver Framework

## Slide 19: Source-Path-Receiver Framework
Propulsion System
Payload
Payload
Coupling

## Slide 20: Source-Path-Receiver Framework
Propulsion System
Payload
Payload
Receiver – vibration on important components in the payload
Coupling

## Slide 21: Source-Path-Receiver Framework
Propulsion System
Payload
Payload
Receiver – vibration on important components in the payload
Source – forces acting on the system
Coupling

## Slide 22: Source-Path-Receiver Framework
Propulsion System
Payload
Payload
Receiver – vibration on important components in the payload
Source – forces acting on the system
Path – how energy moves in the system
Coupling

## Slide 23: Source-Path-Receiver Framework
Propulsion System
Payload
Payload
Receiver – vibration on important components in the payload
Source – forces acting on the system
Path – how energy moves in the system
Coupling

## Slide 24: Source-Path-Receiver Framework
Propulsion System
Payload
Payload
Source Component
Path
Receiver Component
TPA groups the sources, paths, and receivers into sub-components of the system
Coupling

## Slide 25: Source-Path-Receiver Framework – The Rules
The receiver cannot generate noise and vibration on its own
The source is the only thing that generates noise and vibration energy
We don’t care about the noise and vibration response on the source
Any source-path-receiver breakdown is valid as long as it follows some simple rules – choose what is most convenient

## Slide 26: Source-Path-Receiver Framework – The Rules
The receiver cannot generate noise and vibration on its own
The source is the only thing that generates noise and vibration energy
We don’t care about the noise and vibration response on the source
Any source-path-receiver breakdown is valid as long as it follows some simple rules – choose what is most convenient

## Slide 27: Source-Path-Receiver Framework – The Rules
The receiver cannot generate noise and vibration on its own
The source is the only thing that generates noise and vibration energy
We don’t care about the noise and vibration response on the source
Any source-path-receiver breakdown is valid as long as it follows some simple rules – choose what is most convenient

## Slide 28: Source-Path-Receiver Framework – The Rules
The receiver cannot generate noise and vibration on its own
The source is the only thing that generates noise and vibration energy
We don’t care about the noise and vibration response on the source
Any source-path-receiver breakdown is valid as long as it follows some simple rules – choose what is most convenient

## Slide 29: Types of TPA

## Slide 30: TPA and One-way FBS
Propulsion System
Payload
Payload
Coupling

## Slide 31: TPA and One-way FBS
Propulsion System
Payload
Payload
Coupling

## Slide 32: TPA and One-way FBS
Propulsion System Only Information
Payload Only Information

## Slide 33: TPA and One-way FBS
Propulsion System Only Information
Payload Only Information

## Slide 34: TPA and One-way FBS
Propulsion System Only Information
Payload Only Information

## Slide 35: TPA and One-way FBS
Propulsion System Only Information
Payload Only Information

## Slide 36: TPA and One-way FBS
Propulsion System Only Information
Payload Only Information

## Slide 37: TPA and One-way FBS
Propulsion System Only Information
Payload Only Information

## Slide 38: TPA and One-way FBS
Propulsion System
Payload
Payload
Coupling

## Slide 39: TPA and One-way FBS – Force Reconstruction
Propulsion System
Payload
Payload
Coupling
Estimate the actual forces acting on the rocket

## Slide 40: TPA and One-way FBS – Classical TPA
Propulsion System
Payload
Payload
Coupling
Estimate the coupling force that is acting on the payload

## Slide 41: TPA and One-way FBS – Classical TPA
Payload
Payload
Estimate the coupling force that is acting on the payload

## Slide 42: TPA and One-way FBS – Component Based TPA
Propulsion System
Payload
Payload
Coupling
Estimate forces that influence the propulsion system in the same way as the rocket motor force

## Slide 43: TPA and One-way FBS – Component Based TPA
Estimate forces that influence the propulsion system in the same way as the rocket motor force
Propulsion System
Payload
Payload
Coupling

## Slide 44: TPA and One-way FBS – Component Based TPA
Estimate forces that influence the propulsion system in the same way as the rocket motor force
Propulsion System
Payload
Payload
Coupling

## Slide 45: TPA and One-way FBS – Component Based TPA
Substructuring explains why component based TPA works but no substructuring is required in the process
The estimated forces in component based TPA are representative of the actual forces acting on the source component
The estimated forces in component based TPA are independent of the receiver component

## Slide 46: Summary
TPA combines many elements of structural dynamics to understand the noise and vibration in systems
Classical TPA:
  Typically focused on troubleshooting noise and vibration issues
  Estimating the coupling forces between the source and receiver
Component based TPA
  Estimating a pseudo-force that is mathematically equivalent to the actual source
  Pseudo-forces are independent of the receiver system
  Makes it possible to estimate noise and vibration responses on untested system configurations
A major challenge with TPA is the force estimation step

## Slide 47: Next Up: Virtual Point Transformation