## Slide 1: Module 3: Frequency Based Substructuring

## Slide 2: FBS: Outline
General introduction to FBS and the problem form
Deriving the FBS equations with simple math/physics
  One-way FBS
  Two-way FBS
Deriving the Lagrange multiplier FBS equations
  Algebraic derivation
  Constrained optimization (akin to Lagrangian mechanics)

## Slide 3: Example System for FBS Derivation

## Slide 4: Example System for FBS Derivation
System A
System B

## Slide 5: Assemble the FRFs in Block Diagonal Format

## Slide 6: Add the Coupling Force at the Interface DOFs
Coupling Force

## Slide 7: Define the Compatibility Condition for the Forces
The FRFs are coupled by estimating coupling forces that satisfy interface compatibility and force equilibrium
Interface Compatibility
Force Equilibrium

## Slide 8: Apply the Compatibility Condition to the Equations
Applying the compatibility condition to the block diagonal FRFs makes it easy to see a path for estimating the coupling force

## Slide 9: Basic FBS Derivation

## Slide 10: FBS Derivation with Basic Linear Algebra
FBS can be derived with a basic understanding of:
  Basic linear algebra
  Newton’s second law
  Frequency response functions
There are two forms of FBS
  One-way – Computes FRFs with responses on one component and forces on another component
  Two-way – Computes FRFs with responses and forces on all components
We’ll first show the derivation with basic math, then introduce LM-FBS

## Slide 11: Solve the System of Equations to Find the Coupling Force

## Slide 12: Solve the System of Equations to Find the Coupling Force
Gather external and coupling forces together
Convert back to matrix notation
Solve for the coupling force
1.)
2.)
3.)
The coupling force is all we need to solve the substructuring problem

## Slide 13: One-way FBS

## Slide 14: Deriving One-way FBS
System A
System B
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA

## Slide 15: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 16: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 17: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 18: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 19: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 20: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 21: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B

## Slide 22: Deriving One-way FBS
One-way FBS is only concerned with responses on system B due to forces on system A and is particularly useful in TPA
System A
System B
Coupled FRF Matrix

## Slide 23: Two-way FBS

## Slide 24: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 25: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 26: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 27: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 28: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system
Multiply

## Slide 29: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 30: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 31: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system

## Slide 32: Deriving Two-way FBS
System A
System B
Two-way FBS is the full substructuring problem and computes FRFs between all the DOFs in the coupled system
Coupled FRF Matrix

## Slide 33: Summarizing the FBS Process

## Slide 34: FBS Process Summary
Define constraints for interface compatibility and force equilibrium
  Responses at coupling DOFs must be the same
  Forces at coupling DOFs must be equal and opposite
Apply the constraints to the block diagonal FRF equation of motion
Solve for the coupling force – some of the literature makes the math look really fancy, but it can be done with simple algebra
Apply the coupling force to the original FRF based equation of motion

## Slide 35: FBS Process Summary
Define constraints for interface compatibility and force equilibrium
  Responses at coupling DOFs must be the same
  Forces at coupling DOFs must be equal and opposite
Apply the constraints to the block diagonal FRF equation of motion
Solve for the coupling force – some of the literature makes the math look really fancy, but it can be done with simple algebra
Apply the coupling force to the original FRF based equation of motion

## Slide 36: FBS Process Summary
Define constraints for interface compatibility and force equilibrium
  Responses at coupling DOFs must be the same
  Forces at coupling DOFs must be equal and opposite
Apply the constraints to the block diagonal FRF equation of motion
Solve for the coupling force – some of the literature makes the math look really fancy, but it can be done with simple algebra
Apply the coupling force to the original FRF based equation of motion

## Slide 37: FBS Process Summary
Define constraints for interface compatibility and force equilibrium
  Responses at coupling DOFs must be the same
  Forces at coupling DOFs must be equal and opposite
Apply the constraints to the block diagonal FRF equation of motion
Solve for the coupling force – some of the literature makes the math look really fancy, but it can be done with simple algebra
Apply the coupling force to the original FRF based equation of motion

## Slide 38: A Closer Look at the Equation
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 39: A Closer Look at the Equation
Block Diagonal FRF Matrix
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 40: A Closer Look at the Equation
Block Diagonal FRF Matrix
Response/Coupling FRFs
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 41: A Closer Look at the Equation
Block Diagonal FRF Matrix
Response/Coupling FRFs
Coupling/Coupling FRFs
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 42: A Closer Look at the Equation
Block Diagonal FRF Matrix
Response/Coupling FRFs
Coupling/Coupling FRFs
Coupling/Force FRFs
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 43: A Closer Look at the Equation
Block Diagonal FRF Matrix
Response/Coupling FRFs
Coupling/Coupling FRFs
Coupling/Force FRFs
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 44: A Closer Look at the Equation
Block Diagonal FRF Matrix
Response/Coupling FRFs
Coupling/Coupling FRFs
Coupling/Force FRFs
The equation has a pattern, with distinct information in the different vector/matrix quantities
The coupling forces are estimated via an inverse problem, which requires special attention
FBS results in duplicate response/reference DOFs at the coupling, since the method doesn’t reshape the FRF matrix

## Slide 45: LM-FBS – Algebraic Derivation

## Slide 46: LM-FBS – The Standard FBS Method
LM-FBS is arguably the most common FBS method
B matrix is the same as the other domains if the response and reference DOFs are the same on all the components
Different B matrices for references and responses if they have different DOFs in the FRFs
You should use this method when using FBS in practice

## Slide 47: LM-FBS – The Standard FBS Method
LM-FBS is arguably the most common FBS method
B matrix is the same as the other domains if the response and reference DOFs are the same on all the components
Different B matrices for references and responses if they have different DOFs in the FRFs
You should use this method when using FBS in practice

## Slide 48: LM-FBS – The Standard FBS Method
LM-FBS is arguably the most common FBS method
B matrix is the same as the other domains if the response and reference DOFs are the same on all the components
Different B matrices for references and responses if they have different DOFs in the FRFs
You should use this method when using FBS in practice

## Slide 49: LM-FBS – The Standard FBS Method
LM-FBS is arguably the most common FBS method
B matrix is the same as the other domains if the response and reference DOFs are the same on all the components
Different B matrices for references and responses if they have different DOFs in the FRFs
You should use this method when using FBS in practice

## Slide 50: LM-FBS – The Standard FBS Method
LM-FBS is arguably the most common FBS method
B matrix is the same as the other domains if the response and reference DOFs are the same on all the components
Different B matrices for references and responses if they have different DOFs in the FRFs
You should use this method when using FBS in practice

## Slide 51: Defining the LM-FBS Compatibility Condition
The LM-FBS derivation is the same as before, but with a change in how we express the compatibility condition
Interface Compatibility
Force Equilibrium

## Slide 52: Making the B Matrices – Interface Compatibility
System A
System B
Interface Compatibility
Select a to enforce interface compatibility:
Which should be equivalent to applying this constraint:

## Slide 53: Making the B Matrices – Interface Compatibility
System A
System B
Interface Compatibility
Select a to enforce interface compatibility:
Which should be equivalent to applying this constraint:
Negative sign could be flipped

## Slide 54: Making the B Matrices – Force Equilibrium
System A
System B
Force Equilibrium
Select a to enforce force equilibrium with a Lagrange Multiplier:
Where:

## Slide 55: Making the B Matrices – Force Equilibrium
System A
System B
Force Equilibrium
Select a to enforce force equilibrium with a Lagrange Multiplier:
Where:
Negative sign could be flipped

## Slide 56: Deriving LM-FBS
Interface Compatibility
Force Equilibrium

## Slide 57: Deriving LM-FBS
1.)
2.)
3.)
4.)
5.)
6.)
7.)
8.)
9.)
10.)
Starting point

## Slide 58: Deriving LM-FBS
1.)
2.)
3.)
4.)
5.)
6.)
7.)
8.)
9.)
10.)
Apply force equilibrium

## Slide 59: Deriving LM-FBS
1.)
2.)
3.)
4.)
5.)
6.)
7.)
8.)
9.)
10.)
Pre-multiply by the response B matrix

## Slide 60: Deriving LM-FBS
1.)
2.)
3.)
4.)
5.)
6.)
7.)
8.)
9.)
10.)
Apply Interface compatibility and solve for λ

## Slide 61: Deriving LM-FBS
1.)
2.)
3.)
4.)
5.)
6.)
7.)
8.)
9.)
10.)
Apply the solved λ to the equation from step two and extract the coupled FRFs

## Slide 62: Comparing LM-FBS and the Basic Derivation
LM-FBS and the basic derivation result in the same equations, with the same patterns

## Slide 63: LM-FBS – Lagrange Multipliers

## Slide 64: LM-FBS as a Constrained Optimization
Quadratic program (akin to Lagrangian mechanics)
KKT system with Lagrange Multipliers
Extracting the first row from the KKT system
Converting from dynamic impedance to FRFs

## Slide 65: LM-FBS as a Constrained Optimization
Quadratic program (akin to Lagrangian mechanics)
KKT system with Lagrange Multipliers
Extracting the first row from the KKT system
Converting from dynamic impedance to FRFs

## Slide 66: LM-FBS as a Constrained Optimization
Quadratic program (akin to Lagrangian mechanics)
KKT system with Lagrange Multipliers
Extracting the first row from the KKT system
Converting from dynamic impedance to FRFs

## Slide 67: LM-FBS as a Constrained Optimization
Quadratic program (akin to Lagrangian mechanics)
KKT system with Lagrange Multipliers
Extracting the first row from the KKT system
Converting from dynamic impedance to FRFs

## Slide 68: Data Requirements for FBS

## Slide 69: Data Requirements for FBS
Need enough response and reference DOFs to fully define the coupling condition – rotations matter
Extra response and reference DOFs can be added, depending on how we want to model the system
System A
System B

## Slide 70: FBS Summary

## Slide 71: FBS - Summary
Conversion to the frequency domain means that the substructuring problem can be solved with basic linear algebra
LM-FBS should be used in practice – note that some literature will use different names for the same method
The B matrices in LM-FBS can be slightly different than other substructuring domains, depending on the response and reference DOFs that exist in the FRFs
Need reference and responses to define the coupling condition, everything else is up to the practitioner

## Slide 72: FBS - Summary
Conversion to the frequency domain means that the substructuring problem can be solved with basic linear algebra
LM-FBS should be used in practice – note that some literature will use different names for the same method
The B matrices in LM-FBS can be slightly different than other substructuring domains, depending on the response and reference DOFs that exist in the FRFs
Need reference and responses to define the coupling condition, everything else is up to the practitioner

## Slide 73: FBS - Summary
Conversion to the frequency domain means that the substructuring problem can be solved with basic linear algebra
LM-FBS should be used in practice – note that some literature will use different names for the same method
The B matrices in LM-FBS can be slightly different than other substructuring domains, depending on the response and reference DOFs that exist in the FRFs
Need reference and responses to define the coupling condition, everything else is up to the practitioner

## Slide 74: FBS - Summary
Conversion to the frequency domain means that the substructuring problem can be solved with basic linear algebra
LM-FBS should be used in practice – note that some literature will use different names for the same method
The B matrices in LM-FBS can be slightly different than other substructuring domains, depending on the response and reference DOFs that exist in the FRFs
Need reference and responses to define the coupling condition, everything else is up to the practitioner

## Slide 75: Next Up: Component Mode Synthesis