## Slide 1: Module 4: Component Mode Synthesis

## Slide 2: CMS: Outline
The “What” and “Why” of Component Mode Synthesis
Theory and Examples with Free-Boundary CMS
Modal Truncation Example

## Slide 3: Domains for Substructuring
large unwieldy matrices
difficult interface measurements

## Slide 4: Domains for Substructuring
Substructuring may seem simple with small spring-mass systems.
Unfortunately most industrial problems involve complex assemblies of intricate subsystems and components.
The physical mass and stiffness matrices can be quite cumbersome to use for physical coupling.
Wouldn’t it be nice if we could couple two reduced-order models (ROMs) of our systems so that the dynamic information we care about is preserved but the computational costs were small?

## Slide 5: The “What” and “Why” of Component Mode Synthesis

## Slide 6: CMS Basics
Component mode synthesis aims to couple two components (or subsystems) through a pair of reduced-order models.

## Slide 7: CMS Basics
Component mode synthesis aims to couple two components (or subsystems) through a pair of reduced-order models.
A reduced-order model is a simpler representation of a mechanical system often viewed through a set of basis-vectors. Choosing which vectors to keep or remove provides ample means of model reduction.

## Slide 8: CMS Basics
Component mode synthesis aims to couple two components (or subsystems) through a pair of reduced-order models.
A reduced-order model is a simpler representation of a mechanical system often viewed through a set of basis-vectors. Choosing which vectors to keep or remove provides ample means of model reduction.
Transforming form physical to our selected ROM basis set will be essential to our success at using CMS.
For this class, we will look at free-boundary modal models as a ROM for CMS

## Slide 9: What are modes?
Modes are inherent physical properties of all objects
Describe how objects naturally respond to stimulation at different frequencies
The fundamental building blocks of all complex dynamic response
All complex dynamic behavior is a linear superposition of modal responses
=
+
+
…
Response
Mode 1
Mode 2
Mode 3
Individual Modal Deflection Shapes

## Slide 10: Modal Reduction?
Physical Domain
Modal Domain
Sensor 101
Sensor 102
Sensor 103
Sensor 104
Sensor 105
Sensor 106
Sensor 107
Sensor 108
q1 Response
q2 Response
q3 Response
Time [s]
We take many responses in the physical domain…
and apply a modal transformation to convert to the modal domain.
If we retain all of the modes this is exact – this is where we use engineering judgement to select the right modes to reduce the model size while retaining prediction accuracy

## Slide 11: Informal Formal Discussion
What size finite element models do your normally see in your field of work?
How many modes of interest are there?
Are modes typically measured to update/validate your finite element models?

## Slide 12: Theory and Examples with CMS

## Slide 13: Example System for CMS
Let’s look at the same example

## Slide 14: Three Steps to Substructuring with CMS
Step 1) Define Uncoupled Equations of Motion (but in the modal domain)
Modal damping
Block diagonal identity matrix
Natural Frequency
Applied modal forces
Whoa, whoa, whoa… where did this equation come from?

## Slide 15: Three Steps to Substructuring with CMS
Physical Domain Description of System a
Pre-multiply by Phi-transpose
Apply modal transform
Repeat for each subsystem and stack matrices in block diagonal form

## Slide 16: Three Steps to Substructuring with CMS
Step 2) Define constraints in physical domain then cast to ROM coordinates
Again we’ll use the modal transform to cast our coordinates into the ROM space

## Slide 17: Three Steps to Substructuring with CMS
Step 3) Enforce constraints to convert our uncoupled equations into a synthesized form
New coupled coordinates
Uncoupled ROM coordinates

## Slide 18: 2 DOF Example in MATLAB

## Slide 19: Truth Assembly

## Slide 20: Physical Substructuring
Step 1) Define Uncoupled Equations of Motion
  Block diagonal matrices for each subsystem
Step 2) Define Constraint Equations for Compatibility
  Define signed-Boolean constraint matrix:
  Cast into coupled generalized coordinates:
  Combining the two:
Step 3) Synthesize Equations of motion
  Transform out equations using the matrix
  Solve the synthesized eigen problem to reveal the assembled modes

## Slide 21: Modal Substructuring
Step 1) Define Uncoupled Equations of Motion in Modal Space
  Block diagonal matrices for each subsystem as modal equations of motion
Step 2) Define Constraint Equations for Compatibility
  Define signed-Boolean constraints in physical space:
  Project into the modal domain:
  Cast into coupled generalized coordinates:
  Combining the three:
Step 3) Synthesize Equations of Motion
  Transform out equations using the matrix
  Solve the synthesized eigen problem to reveal the assembled modes
  Transform back to physical space:

## Slide 22: So what do we lose? Nothing?!?! Magic!
Truth
Modal Substructuring
Physical Substructuring
Mode # | Natural Frequency
1 | 10.86
2 | 23.81
3 | 29.85
Mode # | Natural Frequency
1 | 10.86
2 | 23.81
3 | 29.85
Mode # | Natural Frequency
1 | 10.86
2 | 23.81
3 | 29.85

## Slide 23: Informal Formal Discussion
What are the three steps to setting up a substructuring problem?
In CMS our constraints often satisfy which condition? What does this mean about equilibrium?

## Slide 24: Modal Truncation

## Slide 25: Let’s look at a bigger example (10 DOF systems)
ma
ma
ma
ma
…
10 DOF
Mode # | Frequency (Hz)
1 | 0.00
2 | 497.95
3 | 983.63
4 | 1445.10
5 | 1870.98
6 | 2250.79
7 | 2575.18
8 | 2836.16
9 | 3027.31
10 | 3143.91
ma=10 kg
ka= 1e9 N/m

## Slide 26: Let’s look at a bigger example (10 DOF systems)
ma
ma
ma
ma
…
mb
mb
mb
mb
…
10 DOF
10 DOF
Mode # | Frequency (Hz)
1 | 0.00
2 | 497.95
3 | 983.63
4 | 1445.10
5 | 1870.98
6 | 2250.79
7 | 2575.18
8 | 2836.16
9 | 3027.31
10 | 3143.91
Mode # | Frequency (Hz)
1 | 0.00
2 | 609.86
3 | 1204.70
4 | 1769.87
5 | 2291.47
6 | 2756.64
7 | 3153.94
8 | 3473.57
9 | 3707.68
10 | 3850.49
ma=10 kg
ka= 1e9 N/m
mb=8 kg
kb= 1.2e9 N/m

## Slide 27: Let’s look at a bigger example (10 DOF systems)
ma
ma
ma
ma
…
mb
mb
mb
mb
…
10 DOF
10 DOF
ma=10 kg
ka= 1e9 N/m
mb=8 kg
kb= 1.2e9 N/m
Let’s assume we only have data to 1000 Hz

## Slide 28: Let’s look at a bigger example (10 DOF systems)
ma
ma
ma
ma
…
mb
mb
mb
mb
…
10 DOF
10 DOF
Mode # | Frequency (Hz)
1 | 0.00
2 | 497.95
3 | 983.63
4 | 1445.10
5 | 1870.98
6 | 2250.79
7 | 2575.18
8 | 2836.16
9 | 3027.31
10 | 3143.91
Mode # | Frequency (Hz)
1 | 0.00
2 | 609.86
3 | 1204.70
4 | 1769.87
5 | 2291.47
6 | 2756.64
7 | 3153.94
8 | 3473.57
9 | 3707.68
10 | 3850.49
ma=10 kg
ka= 1e9 N/m
mb=8 kg
kb= 1.2e9 N/m
Let’s assume we only have data to 1000 Hz

## Slide 29: Let’s look at a bigger example (10 DOF systems)
ma
ma
ma
ma
…
mb
mb
mb
mb
…
10 DOF
10 DOF
Truth
Modal Substructuring
Mode # | Natural Frequency
1 | 0
2 | 289.29
3 | 550.25
4 | 850.88
Mode # | Natural Frequency | Error %
1 | 0 | 0%
2 | 308.43 | +6.6%
3 | 554.13 | +0.7%
4 | 901.91 | +5.9%
Whoa! What’s going on?

## Slide 30: What happened?
We took two 10-DOF systems (20 DOFs) and reduced that to 5 modes (5 DOFs) so errors are caused by modal truncation.
Let’s grab a different number of modes, 5 from each system.
Mode # | Frequency (Hz)
1 | 0.00
2 | 497.95
3 | 983.63
4 | 1445.10
5 | 1870.98
6 | 2250.79
7 | 2575.18
8 | 2836.16
9 | 3027.31
10 | 3143.91
Mode # | Frequency (Hz)
1 | 0.00
2 | 609.86
3 | 1204.70
4 | 1769.87
5 | 2291.47
6 | 2756.64
7 | 3153.94
8 | 3473.57
9 | 3707.68
10 | 3850.49

## Slide 31: Can we pick the right modes?
# modes A: 3
# modes B: 2
# modes A: 5
# modes B: 5
As we include more information we drive down error
A good heuristic is to include content from twice the bandwidth of interest in subcomponent models

## Slide 32: Informal Formal Discussion
Model reduction does remove some information from our subcomponent models. How do we determine if we’ve retained enough information?
If we retain all the modes of the subassemblies is our answer exact?

## Slide 33: Conclusions

## Slide 34: More experimental considerations after lunch!
Transmission Simulator Method
Other ROM forms
Constraint Weakening
Mode Selection
Instrumentation Concerns
Nonlinearities

## Slide 35: CMS Wrap-Up
Component mode synthesis aims to couple two components (or subsystems) through a pair of reduced-order models. How much we can reduce the model and what reduction form are rich engineering decisions.
A reduced-order model is a simpler representation of a mechanical system often viewed through a set of basis-vectors. Choosing which vectors to keep or remove provides ample means of model reduction.
We follow a similar primal assembly to physical substructuring but project our constraints (and coupled solutions) into a reduced domain.

## Slide 36: Next Up – Classroom Examples!