## Slide 1: Module 7: Frame & Wing Structure & Examples

## Slide 2: Background
The substructuring community has a rich history which shares its roots with model reduction and structural modification
Each year we see 4-5 sessions on substructuring at IMAC with various topics including:
  Component Mode Synthesis
  Frequency Based Substructuring
  Transfer Path Analysis
  Model Reduction
  Applications of Substructuring
  Real-time Hybrid Substructuring and many more
In 2012 the AmpAir 600 Wind Turbine was selected as a round-robin substructuring example that many universities and research groups have studied
The Dynamic Substructuring focus group continued organizing IMAC sessions and in 2018 it officially became a technical division.

## Slide 3: Round-Robin Challenge
The Technical Division on Dynamic Substructuring has formed a team to begin creating a new round-robin challenge for researchers to utilize
To develop a structure that suits everyone’s needs the team assembled a list of desired qualities that the round-robin challenge structure should have:
  Interfaces challenging and suited for both FBS and CMS techniques
  Simpler system than the Ampair with more similar dynamics between substructures
  Potential for future circular transfer paths
  Repeatability designed into the interfaces
  Nonlinear dynamics due to joints in the structure should be minimized
  Something that is easy to manufacture and transport
  Structure that is simple to test

## Slide 4: Experimental Substructure (Four-unit frame)
Team developed four unit frame with key features
  Manufactured from one piece of metal of stock
  Subcomponent and shaker attachment points machined into frame
  Adaptable to many types of studies
  Possible circular/recursive transfer path
  Large enough to minimize error due to mass loading
Shown is a 3-unit frame (final design has 4 units)

## Slide 5: What is the “truth” answer?
Truth depends on a lot of factors:
  Assembly procedure
  Frequency range of interest
  Linearity of joints
  And other factors…
The goal of this round-robin isn’t to see which method is the closest to truth
Instead… Round-Robin goals include:
  Fostering collaboration between universities and industrial researchers
  Help researchers focus on how to best approach a substructuring problem when truth is unknown
  Discuss different approaches taken and why some are more suited for specific connection interfaces
  See range of blind predictions to understand the range of answer found using substructuring practices
It depends… but we can learn a lot by comparing and collaborating on methods

## Slide 6: Trial Run
SNL performed a trial run on the “original design” system
  Initially presented results from a numerical study performed while designing the system.
  Then performed experimental analytical hybrid substructuring using the transmission simulator method to connect the 4-unit frame with an analytical model of the rectangular wing.
-
+
Experiment
FEM
=

## Slide 7: Trial Results
  Results were compared to an updated truth FEM model
64.0 Hz
332 Hz
233 Hz
238 Hz
293 Hz
115 Hz
58.8 Hz
98.3 Hz
212 Hz
218 Hz
272 Hz
293 Hz

## Slide 8: Trial Results #2
  Mode matching provided good predictions of mode shape and frequency with some spurious modes
Hybrid Prediction
FEM Result

## Slide 9
Let’s put this mornings lectures to use!
Through the rest of Module 7 we will attempt linear substructuring with real Frame & Wing test data!
Notes: So, the motivation behind my project, was that last year, a lot of work was done practicing substructuring techniques on the test bed at low, linear response levels. But, since there is a bolted joint interface between the wing and frame, we can expect that some degree of nonlinear response will manifest at higher forcing levels. So what we did for this year was to screen the assembly for nonlinear behavior, and then form a nonlinear pseudo-modal model and try to project that nonlinearity through the linear substructuring prediction.

## Slide 10: Substructuring Diagram
  The goal of this example is to take a frame, plate, and thin-wing assembly, and use experimental substructuring to remove the thin-wing and replace it with the thick-wing.
Frame
Plate
Thick Wing, 1/4”
-
+
=
Thin Wing, 1/8”
Transmission
Simulator!
Notes: Here is a diagram to give you an idea of what we’re trying to do with substructuring. [NEXT] The goal is to start with an assembly of the frame, a transmission simulator plate, and the thin rectangular wing, [NEXT] decouple the dynamics of the plate and thin wing, [NEXT] and then replace it by coupling in the plate and thick wing. [NEXT] And then this will give us a prediction of the frame, plate, and thick wing assembly. So in addition to getting a linear prediction, we want to form a nonlinear pseudo-modal model of the original assembly, and project that through to get a prediction of the nonlinear response of the thick wing assembly.

## Slide 11: Experimental Setup
Testing was performed on all three substructures and the truth assembly using hammer impacts and accelerometers – the structure was densely instrumented with accelerometers to characterize modes to at least 1600 Hz.
Lets use these experimental mode sets to complete dynamic substructuring.
Notes: To get the experimental data I needed for each assembly, I did very standard linear modal testing, where the assemblies were suspended with bungee cords and then impacted with a modal hammer. I instrumented with a lot of accelerometers to try and get a good spatial resolution of the mode shapes out to at least 1600 Hz. I initially had washers between the components, but this made the system response too linear. Which is bad in this case since we need to see some sort of nonlinear behavior in order to model and project it. So for all data shown here, there are no washers in the interfaces. And each is held together by 4 steel bolts in the corners of the plate.

## Slide 12: CSM Substructuring Theory – TSM
  To perform CMS substructuring, acquire modal information for each substructure and form EOM.
  Physical constraints are defined connecting both structures to the Plate & Thin-Wing subsystem.
  These constraints are cast to modal domain and softened by projecting each subsystems dynamics through the mode shapes of the Plate & Thin-Wing (or a set of singular vectors).
1: Frame, Plate & Thin-Wing
2: Plate & Thin-Wing
3: Plate & Thick-Wing
Notes: To substructure together each of those experimental subsystems, I used component mode synthesis. So we start with an equation of motion with each of the subsystems initially uncoupled. [NEXT] To tie them together, we define a set of constraints between the overlapping degrees of freedom in each. [NEXT] Usually these sorts of hard constraints lead to poor results, so what we can do is cast them to modal coordinates, and then soften the constraints by projecting them through a representative of the motion at the interface. Where that can be directly mode shapes or an SVD representation of them.

## Slide 13: CSM Substructuring Theory – TSM
  The null space function is used to determine the localization matrix L.
  L-matrix is used to enforce constraints on equation of motion and predict system assembly response.
  An Eigen solution of the Transformed Mass and Stiffness Matrices yield the predicted Natural Frequencies and Mode shapes.
1: Frame, Plate & Thin-Wing
2: Plate & Thin-Wing
3: Plate & Thick-Wing
Notes: So since were trying to constrain motion together and the equations equate to zero, we can solve for the coupling transformation matrix as the null space of that B matrix of constraints. So then we can use that to pre and post multiply the uncouple M and K, and then get the predicted mode shapes and frequencies from an eigensolution of the coupled M and K.

## Slide 14: Choices for the Practioner to Make
  To perform CMS substructuring, acquire modal information for each substructure and form EOM.
  Physical constraints are defined connecting both structures to the Plate & Thin-Wing subsystem.
  These constraints are cast to modal domain and softened by projecting each subsystems dynamics through the mode shapes of the Plate & Thin-Wing.
1: Frame, Plate & Thin-Wing
2: Plate & Thin-Wing
3: Plate & Thick-Wing
Which DOFs should we include in our subtraction and addition steps?
How many modes should we include for each structure?
Should we use for the constraint softening? Or try using singular vectors?
Notes: To substructure together each of those experimental subsystems, I used component mode synthesis. So we start with an equation of motion with each of the subsystems initially uncoupled. [NEXT] To tie them together, we define a set of constraints between the overlapping degrees of freedom in each. [NEXT] Usually these sorts of hard constraints lead to poor results, so what we can do is cast them to modal coordinates, and then soften the constraints by projecting them through a representative of the motion at the interface. Where that can be directly mode shapes or an SVD representation of them.

## Slide 15: Data Available Lets Make Some Choices!

## Slide 16: Data is where?
Test Data: FrameWing_Data.mat
MATLAB Script: Mod7_FrameWing_Example.m
  You can change:
    The number of modes in each subsystem
    If the constraints are just in the middle or also on the wings
    If the constraint softening is done with modes or singular vectors
  Vary each and check the results that come up in the MAC and FRF plots

## Slide 17: Substructuring Diagram
  The goal of this example is to take a frame, plate, and thin-wing assembly, and use experimental substructuring to remove the thin-wing and replace it with the thick-wing.
Frame
Plate
Thick Wing, 1/4”
-
+
=
Thin Wing, 1/8”
Notes: Here is a diagram to give you an idea of what we’re trying to do with substructuring. [NEXT] The goal is to start with an assembly of the frame, a transmission simulator plate, and the thin rectangular wing, [NEXT] decouple the dynamics of the plate and thin wing, [NEXT] and then replace it by coupling in the plate and thick wing. [NEXT] And then this will give us a prediction of the frame, plate, and thick wing assembly. So in addition to getting a linear prediction, we want to form a nonlinear pseudo-modal model of the original assembly, and project that through to get a prediction of the nonlinear response of the thick wing assembly.

## Slide 18: Discussion of in class exercise
Notes: So since were trying to constrain motion together and the equations equate to zero, we can solve for the coupling transformation matrix as the null space of that B matrix of constraints. So then we can use that to pre and post multiply the uncouple M and K, and then get the predicted mode shapes and frequencies from an eigensolution of the coupled M and K.

## Slide 19: Linear Results
  Predictions led to low frequency and damping error outside of a few modes.
Mode Number | Truth |  | Prediction |  | Error |  | MAC
 | fn | zt | fn | zt | fn | zt | 
1 | 127.8 | 0.23 | 126.3 | 0.69 | -1.2% | 201.2% | 0.99
2 | 236.2 | 0.35 | 232.3 | 0.85 | -1.7% | 144.8% | 0.96
3 | 237.6 | 0.78 | 238.6 | 0.50 | 0.4% | -35.8% | 0.97
4 | 356.1 | 0.70 | 351.6 | 0.40 | -1.3% | -42.3% | 0.97
5 | 439.4 | 0.51 | 436.6 | 0.31 | -0.6% | -38.5% | 0.91
6 | 454.6 | 0.59 | 466.2 | 0.81 | 2.6% | 38.2% | 0.77
7 | 463.1 | 0.06 | 444.8 | 0.32 | -4.0% | 444.9% | 0.99
8 | 643.0 | 0.99 | 616.4 | 0.47 | -4.1% | -52.2% | 0.95
9 | 728.9 | 0.30 | 682.3 | 0.62 | -6.4% | 105.3% | 0.97
10 | 733.5 | 0.58 | 706.5 | 0.34 | -3.7% | -41.8% | 0.96
11 | 833.7 | 0.13 | 832.9 | 0.25 | -0.1% | 96.3% | 0.97
12 | 910.2 | 0.90 | 893.0 | 0.61 | -1.9% | -31.9% | 0.99
Notes: Here are the linear substructuring predictions, where I guess you could say it’s a cheated or informed answer, where I had the truth data and tuned the content in each subsystem to best match that. I think its justified here because the focus of this work is on the viability of the nonlinear projection, so having the best linear prediction helps in narrowing in on that result which ill show later. So, we have good results out to about 100 Hz, with mostly under 3 or 4 percent error. The damping is admittedly all over the place, but it was also the same when trying to measure it experimentally, where the nonlinearity in the joint kept causing the linear value to shift around and it didn’t really settle. And the MAC values are pretty good too.
Modes Kept: FPThin: 1-20 855 Hz, Pthin:1-17 1067 Hz , Pthick: 1-25 3600 Hz

## Slide 20: Another Example from the Wiki - Thin Wing to Swept Wing -

## Slide 21: Substructuring Diagram
  The goal of this example is to take a frame, plate, and thin-wing assembly, and use experimental substructuring to remove the thin-wing and plate, then replace it with the swept wing
  We wanted to perform this prediction blind without measuring truth and develop tools and habits for successful blind substructuring.
-
=
+
FEM
EXP
EXP

## Slide 22: Swept Wing Model Generation
  Swept wing component testing was completed at Linnæus university in order to update a finite element model which would be sent to partners at Sandia
  10 swept wings are available for Dynamic Substructuring Participants with ongoing measurements to understand their variability!
  A finite element model was updated to best match Swept Wing test data and provided to SNL to make initial substructuring predictions
Swept Wing No. | Mass [g] | t [mm] | f1 [Hz] | f2 [Hz] | f3 [Hz]
1 (@ Sandia) | 1169.1 | 3.0 | 69.3 | 105.7 | 182.6
2 | 1164.0 | 3.0 | 69.1 | 105.2 | 181.9
3 | 1165.0 | 3.0 | 69.1 | 105.4 | 181.9
4 | 1169.1 | 3.1 | 69.2 | 105.6 | 182.6
5 | 1164.2 | 3.0 | 69.1 | 105.3 | 181.9
6 | 1164.4 | 3.0 | NA | NA | NA
7 | 1169.9 | 3.0 | NA | NA | NA
8 | 1166.3 | 3.0 | NA | NA | NA
9 | 1169.6 | 3.0 | NA | NA | NA
10 | 1169.4 | 3.1 | NA | NA | NA

## Slide 23: Frame, Plate, and Thin-Wing Experiments
  Aluminum frame, plate, and thin-wing component assemblies were tested at Sandia.
  Linear free responses were measured with accelerometers and curve fit with ATA Opoly.
  Significant modes out to 1600 Hz were measured and fit to provide a rich modal basis for substructuring.
  Data also used in companion project exploring incorporating nonlinear behavior into substructuring predictions that that will be presented later.

## Slide 24: Substructuring Theory
  To perform CMS substructuring, acquire modal information for each substructure and form EOM.
  Constraints are defined connecting both structures to the TS (Thin Wing and Plate) system.
  The null space function is used to determine the synthetization matrix L.
  L-matrix used to enforce constraints on equation of motion and predict system assembly response.

## Slide 25: Initial Substructuring Results
  We set our initial goal to predict modes blindly out to 500 Hz
  Using previous heuristics we retained modes of each subassembly out to 1,000 Hz to ensure we included the proper modes
  cond() = 41.31
  Frame, Plate, Wing: 23 modes
  Plate and Wing: 16 modes
  Plate and Swept Wing: 20 modes
Prediction | 
fn [Hz] | zt
0.00 | 0.04%
0.03 | 0.03%
0.05 | 0.04%
0.06 | 0.08%
0.06 | 0.13%
0.08 | 0.26%
0.09 | 0.86%
53.26 | 1.03%
67.63 | 4.72%
202.15 | 0.17%
235.34 | -6.02%
288.27 | -6.02%
363.56 | 0.75%
402.58 | 0.77%
416.43 | 0.57%
416.43 | 0.57%
439.75 | 0.65%
448.39 | 1.36%
Excess Rigid Modes
Spurious Modes
Imaginary Eigen Frequencies!
Negative Damping?

## Slide 26: Tricks and Checks 1: Rigid Check
  Attempt substructuring with just rigid modes to check if connections are incorrect and shape/geometry documentation are in line
  cond() = 6.2
  Frame, Plate, Wing: 6 modes
  Plate and Wing: 6 modes
  Plate and Swept Wing: 6 modes
Prediction | 
fn [Hz] | zt
0.026 | 0.04%
0.053 | 0.03%
0.054 | 0.02%
0.057 | 0.04%
0.075 | 0.04%
0.079 | 0.04%
Rigid modes substructure as expected!

## Slide 27: Tricks and Checks 2: Modal Space Check
  Check to ensure modes when partitioned down to the connection degrees of freedom span the space for the structures included!
  Here – we can see we don’t have the right information in the TS (Plate and Wing Subassembly) to describe the interface motion of the baseline assembly for mode 23!
  Let’s truncate our baseline assembly down to 20 modes (and the subpieces down to 14) so we are only including modes we need to span the space

## Slide 28: Updated Substructuring Results
  cond() = 15.99
  Frame, Plate, Wing: 20 modes
  Plate and Wing: 14 modes
  Plate and Swept Wing: 14 modes
  ✔ Correct number of rigid modes
  ✔ No imaginary eigen values or damping issues
  Better modal independence in self-MAC
Initial Prediction | Updated Prediction
fn [Hz] | fn [Hz]
0.00 | 0.03
0.03 | 0.05
0.05 | 0.05
0.06 | 0.06
0.06 | 0.07
0.08 | 0.08
0.09 | 42.69
53.26 | 65.88
67.63 | 173.93
202.15 | 223.33
235.34 | 260.63
288.27 | 325.94
363.56 | 371.69
402.58 | 442.23
416.43 | 518.81
416.43 | 603.64
439.75 | 631.52
448.39 | 814.78

## Slide 29: “Truth” Comparison
  Blind Prediction results concluded with fairly accurate estimate!
Prediction Modal Index | Predicted | Truth | Error | MAC
1 | 42.78 | 49.33 | -13.3% | 0.98
2 | 65.99 | 66.25 | -0.4% | 0.99
3 | 174.1 | 181.4 | -4.0% | 0.95
4 | 223.9 | 226.8 | -1.3% | 0.96
5 | 260.7 | 259.5 | 0.5% | 0.95
6 | 326.4 | 293.1 | 11.4% | 0.89
7 | 371.7 | 389.1 | -4.5% | 0.76
8 | 442.7 | 425.5 | 4.0% | 0.55
9 | 520.2 | 487.6 | 6.7% | 0.71
10 | 603.9 | 414.1 | 45.8% | 0.58
11 | 631.7 | 619.1 | 2.0% | 0.52

## Slide 30: Linear Results Shape Plots
  Shapes of some of the significant modes
Prediction Elastic Modes 1-4
Truth Elastic Modes 1-4

## Slide 31: Results from Tuning Modal Basis
  Informed Prediction yields better results
    Frame, Plate, Wing: 62 modes
    Plate and Wing: 22 modes
    Plate and Swept Wing: 26 modes
Prediction Modal Index | Predicted | Truth | Error | MAC
1 | 50.93 | 49.33 | 3.2% | 0.99
2 | 67.62 | 66.25 | 2.1% | 0.99
3 | 191.9 | 181.4 | 5.8% | 0.98
4 | 231.8 | 226.8 | 2.2% | 0.97
5 | 269.8 | 259.5 | 4.0% | 0.97
6 | 348.0 | 293.1 | 18.7% | 0.85
7 | 389.6 | 389.1 | 0.1% | 0.90
8 | 420.2 | 414.1 | 1.5% | 0.89
9 | 433.2 | 425.5 | 1.8% | 0.94
10 | 503.0 | 487.6 | 3.2% | 0.79
11 | 548.2 | 509.1 | 7.7% | 0.87
12 | 639.5 | 619.1 | 3.3% | 0.94
13 | 700.0 | 704.5 | -0.6% | 0.44
14 | 738.6 | 669.7 | 10.3% | 0.73
15 | 820.8 | 856.2 | -4.1% | 0.96
16 | 930.1 | 911.0 | 2.1% | 0.39
Notes: Results if we use the truth values to tune in the modal basis selctions

## Slide 32: Let’s take a break